## Slide 1
HandRate: Heart Rate Monitoring While Simply Holding a SmartPhone
Kevin Jiokeng, Gentian Jakllari, André-Luc Beylot IRIT/Toulouse INP-ENSEEIHT, University of Toulouse, France – Email: firstname.lastname@toulouse-inp.fr IEEE PerCom’21 – March 25th, 2021

## Slide 2: Context
Heart Rate Monitoring: early identification and prevention of heart diseases
⇒ Multiple medical devices (use at hospital or home)
But Cardiovascular Diseases still remain the world’s leading cause of death [AHA, 2018] → 22M+ in 2030
Notes: (>22M in 2030)

## Slide 3: Context
Existing approaches with a Smartphone:
  Adding specialized sensors
  -- Not accessible to a wide range of users
  Using built-in sensors:
    Ordinary camera as a PPG sensor
    IMU with phone on the chest or the navel
-- Require active user participation
Sensing
+
Processing power
_____________
Always with us

## Slide 4: HandRate
Heart Rate Monitoring without active user participation
HandRate revisits Ballistocardiography (BCG)
- Measurement of the body movement during cardic cycle - Caused by recoil forces (espcially during the systole)
Two important questions :
  Is it possible to acquire BCG in hand with a commodity mobile phone ? Far away from the heart and subject to motion artifacts
  If yes, which system to extract Heart Rate from it ?

## Slide 5: Outline
Introduction: Context, Existing approaches and Questions
Hand-BCG: Feasability Study
HandRate: Our System
Performance Evaluation
Conclusion

## Slide 6: Hand-BCG: is it possible?
The theoretical answer
  Smartphones’ accelerometers are able to sense very weak motions
    Typical sensitivity value: 2 x 10-3 m.s-2
  Peaks’ average in our dataset: 9 x 10-2 m.s-2
    barely an order of magnitude greater than the accelerometers’ noise level (~2 x 10-2 m.s-2)

## Slide 7: Hand-BCG: is it possible?
Experimental study
  Collection of multiple signals: 30s per session
  Hand vs Navel (reference)
  Frequency domain analysis
    Computation of signal quality : Qkurt [1]
[1] R. Mohamed and M. Youssef, “Heartsense: Ubiquitous Accurate Multi-Modal Fusion-based Heart Rate Estimation Using Smartphones” ACM IMWUT, 2017

## Slide 8: Hand-BCG: Opportunities and challenges
BCG signal can be sensed from hand using a smartphone’ accelerometer
But this signal can be of poor quality, making Heart Rate computation challenging

## Slide 9: Outline
Introduction: Context, Existing approaches and Questions
Hand-BCG: Feasability Study
HandRate: Our System
Performance Evaluation
Conclusion

## Slide 10: HandRate
Heart Rate Monitoring system with phone in hand
Just takes as input the accelerometer readings to compute the Heart Rate

## Slide 11: Preprocessing
Denoising
Normalization
Resampling
Filtering
Filtering out too weak or too strong signals
--> in the range [-1, 1]
--> Fs = 100Hz
Reduce noise
Applied on each of the 3 axes independently

## Slide 12: Signal Recomposition
Problem: the axis that best measures the signal depends on how the user holds the phone
Two possible approaches :
  Process (each of the axes) + Combine (the results)
  Combine (the axes) + Process (the resulting 1D signal)
Choice: Principal Component Analysis

## Slide 13: Signal Recomposition
Evaluation
  105 volunteers
  30s per volonteer
  Apply PCA and compute the amount of variance retained on each dimension
92.1% of variance retained on the first PC

## Slide 14: Signal Analysis
Processing options (for the 1D signal):
  Purely in the time domain. But not clear peaks
  Purely in the frequency domain
Time-frequency approach:
  Spectrogram (Short Time Fourier Transform)
  Scalogram (Continuous Wavelet Transform) because of events better localized in time

## Slide 15: Heartbeat Identification

## Slide 16: Heartbeat Identification
Straightforward approach: "flatten" the scalogram by taking the maximum value of each timestep
  Mixed results (like the quality of the data)
Neural network:
  Model capable of predicting the heartbeat instant
  Based on the ECG measured at the same time

## Slide 17: Heartbeat Identification
About the NN model:
  Encoder-decoder architecture (seq2seq)
  Processing by sliding windows of 3s (2s stride)
  Not big model: ~ 236k parameters
Combatting dataset imbalance:
  Weighted loss function (greater weight for ‘1’)
  Multiple ‘1’ for a single peak

## Slide 18: Outline
Introduction: Context, Existing approaches and Questions
Hand-BCG: Feasability Study
HandRate: Our System
Performance Evaluation
Conclusion

## Slide 19: Evaluation: Setup
The data:
  18 participants, 10+ sessions per person
  Fairly varied dataset: covers the range of 54 - 106 bpm
Two versions of HandRate:
  general model (HandRate-g)
  personalized model (HandRate-p)
Comparison with:
  FFT-based: search for the most active freq. in the FFT spectrum
  Xcorr-based: cross-correlation between the signal and a template, and taking the peaks
  CWT-based: Downsampling of the scalogram and selection of peaks
  Other systems (SCG, PPG, special sensors)

## Slide 20: Evaluation: Results
HandRate performs better (median of 2.9 bpm) And HandRate-p even more (median of 2 bpm)
HandRate achieves results comparable to techniques that require special sensors and/or active participation
FFT-based

## Slide 21: Evaluation: Results
HandRate(-g) performs well in different experimental conditions
And runs in real time (~200ms of processing time every 2 seconds)

## Slide 22: Outline
Introduction: Context, Existing approaches and Questions
Hand-BCG: Feasability Study
HandRate: Our System
Performance Evaluation
Conclusion

## Slide 23: Conclusion
Heart rate monitoring system with a phone in hand
  Feasibility study
  Design of a system to perform this task
  Performance evaluation - Error comparable to other techniques and performs well under different experimental conditions
Future work
  More diverse data collection and evaluation (large period of time in daily life, phone models, non-healthy subjects)

## Slide 24
Thank you for your attention.
And for your questions :)